## Slide 1: DSP Assignment-5 Changing Sampling Rate with FFT Filters
Assigned 2022/1/12

## Slide 2: Objective
To understand up-sampling and down-sampling techniques
To implement an FFT low-pass filter with overlap-add method

## Slide 3: Specification
T = 1/44100 sec for input signal
TM/L = 1/8000 sec for output signal
Input signal x[n]: input.wav, a stereo music file (44.1kHz, 16bits)
Output signal : output.wav, a stereo music file (8kHz, 16bits)

## Slide 4: Low-Pass Filter
The low-pass filter is implemented by an FFT filter.
The signal is filtered by the FFT filter in a frame-by-frame manner.
We first segment into segments of P points, i.e.,
where

## Slide 5: Low-Pass Filter
Then, the low-pass filtering in time domain can be expressed by
where
The low-pass filtering in frequency domain is expressed by
where
and are the N point FFT of and and

## Slide 6: Parameters of FFT filter
P=960  We process each frame with 960 samples
Q=1024  The length of the low-pass filter
N=2048  and are zero-padded to be lengths of 2048
Actually, we can direct design an ideal low-pass filter by

## Slide 7: Requirement
All the program must be written in C
The low-pass filtering must be implemented by the overlap-add method.
The output.wav can be played by media player
Due: 2022/1/27